## Slide 1
Electricity and Magnetism
AC Circuits
9
AC Sources and Phasors
An alternating current (AC) generator produces an emf that oscillates sinusoidally in time with an angular frequency ω = 2πf and peak emf E0:
The emf, voltage across circuit elements, and current through circuit elements all oscillate in time and can be represented by a phasor. A phasor is a vector that rotates counterclockwise
ωt
value at t
about the origin at angular frequency ω. The instantaneous value of the quantity is the projection of the phasor on the x-axis.
One Element Circuits
Resistor Circuit
A single resistor R connected to an oscillatory emf source E has an instantaneous voltage given by
where VR is the peak voltage. The instantaneous current through the resistor is
where IR is the peak current. The current through and voltage across the resistor are in phase; the peaks occur at the same time.
Capacitor Circuit
A single capacitor C connected to an oscillatory emf source E has an instantaneous voltage given by
The instantaneous current through the resistor is
where IC = ωCVC is the peak current. The current through and voltage across the capacitor are out of phase; the current leads the voltage by π/2 (90°).
R
E
vR
iR
VR
IR
C
E
vC
iC
VC
IC
The capacitive reactance XC is defined to be
and has units of ohms. The peak current can be written as
Inductor Circuit
A single inductor L connected to an oscillatory emf source E has an instantaneous voltage given by
The instantaneous current through the resistor is
where IL = VL/ωL is the peak current. The current through and voltage across the capacitor are out of phase; the current lags the voltage by π/2 (90°).
vL
iL
VL
IL
L
E
The inductive reactance XL is defined to be
and has units of ohms. The peak current can be written as
RC Filter Circuits
The peak current in an RC circuit is
and the voltages across the resistor and capacitor
are
An RC circuit can act as a frequency filter:
The voltage across the capacitor VC → E0 as ω → 0. Connecting an element across the capacitor allows it to act as a low-pass filter: only low frequencies will be transmitted.
The voltage across the resistor VR → E0 as ω → ∞. Connecting an element across the resistor allows it to act as a high-pass filter: only high frequencies will be transmitted.
R
E
C
The Series RLC Circuit
The peak current in an RLC circuit is
where Z is the impendence:
The peak voltages are VR = IR, VC = IXC, and VL = IXL.
The emf and current are out of phase by the phase angle
The maximum current Imax = E0/R through the circuit occurs at the resonance frequency
R
E
C
L
Power
The emf supplies energy to the circuit at the rate
where , , and ϕ is the phase factor.
The average power dissipated by a resistor is
The average power dissipated by a capacitor or inductor is zero.
Joseph D. MacMillan | Licensed under CC BY-NC-SA 4.0.